REPORT
IAP Assignment 2
Group 14
Bhusan kulkarni 12CS30016
Gaurav Kumar 12CS10020
Ankit Kumar Gupta 12CS10006

---
Q1)

---
Q2)
- Routing table for r1
  IP Netmask Next Hop Interface
- 10.0.1.2 255.255.255.255 10.0.1.2 eth2
- 10.0.1.3 255.255.255.255 10.0.1.3 eth2
- 10.0.2.0 255.255.255.0 10.0.2.1 eth3
- 10.0.3.0 255.255.255.0 10.0.3.1 eth1
- 10.0.4.0 255.255.255.0 10.0.3.1 eth1
  Rotuing table for r2
- IP Netmask Next Hop Interface
- 10.0.2.2 255.255.255.255 10.0.2.2 eth2
- 10.0.1.0 255.255.255.0 10.0.1.1 eth1
- 10.0.3.0 255.255.255.0 10.0.1.1 eth1
- 10.0.4.0 255.255.255.0 10.0.4.1 eth3

---
Q2)
- Routing table for r3
  IP Netmask Next Hop Interface
- 10.0.3.2 255.255.255.255 10.0.3.2 eth3
- 10.0.2.0 255.255.255.0 10.0.1.1 eth1
- 10.0.1.0 255.255.255.0 10.0.1.1 eth1
- 10.0.4.0 255.255.255.0 10.0.4.1 eth2
  Rotuing table for r4
  IP Netmask Next Hop Interface
- 10.0.4.2 255.255.255.255 10.0.4.2 eth2
- 10.0.4.3 255.255.255.255 10.0.4.3 eth2
- 10.0.2.0 255.255.255.0 10.0.2.1 eth3
- 10.0.3.0 255.255.255.0 10.0.3.1 eth1
- 10.0.1.0 255.255.255.0 10.0.3.1 eth1

---
Q3)ping from h1-h2

---
 Ping from h1-h3

---
Ping from h1 to h4

---
Ping from h1 to h5

---
Ping from h1 to h6

---
Q 5,6,7,8
- Refer folder wireshark_screenshot
- You can observe network and destination host
  unreachable behavior
- You can also see trace route behavior in pcap file
- Middle host are sending Time to live exceeded message and final destination is sending Echo
  Reply message

---
Plot of Bandwidth vs throughput (h1-h6) for UDP

---
Plot of bandwidth vs throughput (h1-h2) for UDP

---
Observations from ping h1-H*
- As you can see the ping screen shots that time taken for ping form h1-h* increases with number for hops between h1-h*.
  so ping time for h1-h6 > h1-h2
- For any Ping H1-H* :
  First ping taken more time that subsequent pings since in the first ping router do an ARP query to find next hop HW address after than it caches that address.

---
Observations from ping h2 to unreachable IP
- For this case ICMP reply type to TYPE_DEST_UNREACH
- And then we set code for unreachable in two ways
  - Network unreachable : router first checks whether the destination network exists or not. If it doesn't
    it sets code to CODE_UNREACH_NET
  - Host unreachable : it destination network exists it forwards packet
    to the next Hop using routing table. Once the packet reaches to that
    networks gateway router it checks whether host exists or not. If
    destination Host doesn't exist set
    code to CODE_UNREACH_HOST
    You can see this behavior in the wireshark traces of that ping.

---
Observations from ipef with UDP
- Since every channel has a maximum data rate which it can support hence throughput does not always increase with bandwidth. After some bandwidth it becomes constant. Initially it increases linearly with bandwidth.
- Max. Throughput for H1-H6 UDP – 768 Mb/sec
- Max. Throughput for H1-H2 UDP – 750 Mb/sec

---
Contribution Table
Every one equally contributed to assignment